## Slide 1: CLIMBING SPACE Section 236
OJUA NESC Spring Training
April 19-20, 2011

## Slide 2: Climbing Space
2007 Code change that started this discussion (from 2007 pre-print)
Section 236G
Climbing space past longitudinal runs not on support arms
The full width of climbing space shall be provided past longitudinal runs and shall extend vertically in the same position from 1.0 m (40 in.) below the run to a point 1.0 m (40 in.) above [or 1.50 m (60 in.) where required by Rule 236E]. The width of climbing space shall be measured from the longitudinal run concerned. Longitudinal runs on racks, or cables on messengers, are not considered as obstructing the climbing space if all wires concerned are covered by rubber protective equipment or otherwise guarded as an unvarying practice before workers climb past them. if the location, size, and quantity of the cables permit qualified workers to climb past them. This does not apply where communication conductors are above the longitudinal runs concerned.
Supporting Comment – It is not common for supply workers to cover or guard communication cables before climbing past them. The proposed wording is intended to provide a practical bridge between the Code wording and everyday work practices, and is not intended to reduce safety.

## Slide 3: Climbing Space
REQUEST FOR INTERPRETATION OF THE
NATIONAL ELECTRICAL SAFETY CODE
Name: John Wallace Date: April 30, 2010
Address: 550 Capitol Street NE, Salem, OR 97310
Organization represented: Oregon Public Utility Commission
Rule: 236 Climbing space
Statement of Problem and Supporting Comments:
Rule 236G was modified somewhat in the 2007 edition, deleting the language about covering wires with rubber protective equipment or otherwise guarding them, as an unvarying practice, before climbing past them.
Is this modification meant to change the intent of Rule 236, particularly as it regards placement of communications facilities on a jointly used pole? We have operated under the understanding that the dimensions and location of the climbing space (Rule 236A) would remain the same and that the phrase “climbing space past longitudinal runs” in Rule 236G does not mean that it is now permissible to climb over them, essentially using then as a ladder. Although the climbing space may rotate as a worker ascends the pole, the worker must first climb past the space-limiting cable/conductor.
Is it still necessary to maintain a quarter of the pole as a clear climbing space, consistent with the description provided in Rule 236A?
Signature: ___________________________________

## Slide 4: Climbing Space
(Received March 25, 2011)
NESC IR 563 – Release
Your Interpretation Request asks two questions. The first question is the intent of the Rule 236G revision in the 2007 Edition, particularly regarding placement of communication facilities on a jointly-used pole. The answer is no, the revision was not intended to change placement of communication facilities, including cables, on a jointly-used pole.
For your information, the change was made to reflect common work practices. For the most part, workers were not covering communication cables when climbing past them and it was determined that such action was not a safety issue. Note that energized electric facilities must be covered in accordance with Part 4 Work Rules.
Your second question asks if it is still necessary to maintain a quarter of the pole as a “clear” climbing space, consistent with Rule 236A (emphasis added). The answer is a qualified yes.
Rule 236A was not revised; a climbing space still must be provided on one side or corner of the pole. However, this space is not necessarily “clear” as described in your question. See Rule 236G; note that longitudinal runs of cables on messengers are not considered to obstruct the climbing space if the cables are installed such that qualified workers can climb past the cables.
DEH
9/30/2010

## Slide 5: Climbing Space
Rule 236. Climbing space
A. Location and dimension
1. A climbing space having the horizontal dimensions specified in Rule 236E shall be provided past any conductors, support arms, or other parts.
2. The climbing space need be provided on one side or corner of the support only.
3. The climbing space shall extend vertically past any conductor or other part between levels above and below the conductors as specified in Rules 236E, F, G, and I, but may otherwise be shifted from any side or corner of the support to any other side or corner.
(See next page for visual representation of 236A3)
Rule 236A was not revised by the 2007 Code change, nor by the interpretation.

## Slide 6: Climbing Space
30”
30”
80”
Min.
40” Min.
Overlap
Climbing
Space
40” Min.
Pole

## Slide 7: Climbing Space
Rule 236E. Climbing space between conductors states that “Climbing space between conductors shall not be less than the horizontal dimensions specified in Table 236-1. Those dimensions are intended to provide a clear climbing space of 600mm (24 in.) while the conductors bounding the climbing space are covered with temporarily installed protective covering for the voltage involved. The climbing space shall be provided both along and across the line and shall be projected vertically not less than 1.0 m (40 in.) above and below the limiting conductors”.
(Table 236-1 is reproduced on the following page)

## Slide 8: Climbing Space

## Slide 9: Climbing Space
Conclusions:
The language of IR563 does not alter the OPUC’s interpretation of Section 236.
The 2007 language change did not change the overall intent of Section 236. Specifically, that a clear climbing space (Rule 236E) must be provided on one corner or side of a support structure.
“Boxing” of a pole violates the language and intent of Rules 236G (location), 236E (climbing space between conductors), and is not an acceptable method of construction in Oregon.